Guess Paper – 2009

Class – X
Subject – Physics

[Semiconductor & Devices]

Time – 1hr.

Question no 1 to 5     –  [1 Marks each].                  Question no 6 to 10   – [2 Marks each].

## Question no 11 to 15 – [3 Marks each].                 Question no 16 & 17 – [5 Marks each].

- How does the energy gap of an intrinsic semiconductor vary when doped with a trivalent impurity?

- Draw energy band diagram of n-type semiconductor.

- A semiconductor has equal electron and hole concentration 6×108 /m3 .On doping with a certain impurity, electron concentration increases to 8×1012 /m3 .Identify the type of semiconductor after doping.

- How does the dc current gain of a transistor change, if the width of the base region is increased?

- Why are photodiodes used preferably in reverse bias condition?

- In the working of a transistor, emitter base junction is forward biased, while the collector base junction is reverse biased, why:

- Explain with the help of a circuit diagram, how the thickness of depletion layer in p-n junction diode changes when it is forward biased.

- A transistor can not be used as a rectifier, why?

- In a transistor base is lightly doped and is a thin layer, why?

- What is the condition for the state of saturation of a transistor?

- What is an intrinsic semiconductor? How can this material be converted in to (a) p type (b) n-type extrinsic semiconductor? Explain with the help of energy diagram.

- Explain briefly with the help of a circuit, how V-I characteristics of a p-n junction diode are obtained in (a) Forward bias (b) Reverse bias. Draw the shape of curves obtained.

- In a common emitter transistor amplifier, the input resistance of a transistor is 100 ohm. On changing its base current by 10µA, the collector current increases by 2mA.If a load resistance of 5kilo ohm is used in the circuit, calculate (a) current gain (b) voltage gain of the amplifier

- In a transistor forward bias is always small as compared to Reverse bias. Explain

- Explain the working of a Zener diode.

- Explain the function of base region of a transistor. Draw a circuit diagram to study the input and output characteristics of NPN transistor in a common emitter (CE) configuration. Show these characteristics graphically. Explain how the current amplification factor is calculated from these

Characteristics.

- Explain the working of transistor as an oscillator.

## PHYSICS POINT

E-mail – physicspoint@hotmail.com

Anil Kumar Pandey

Email anilpandey1225@hotmail.com

# Text boxes

FOR – XIth , XIIth  & Competitive Exam.

PP

Physics Point.

(

(

(